| Sl. No | Area of operation | Anticipated risk | Recommended OSH practices | Inputs needed |
| --- | --- | --- | --- | --- |
| 1. | Pre-treatment |
|  | 1.1. | Screens |
|  | 1.2. | Settling chamber | Gas poisoning due to presence of H2S |

Check presence of gas and , if required, ventilate settling chamber/pit before entering

Person entering pit to be secured with life line, loose end held by person outside the pit

lead acetate paper or H2S detection instrument

life line and belt

| first aid kit including Amyl Nitrite capsule |
| --- |
| 2. | Collection system |
|  | 2.1. | Pipelines | Injuries during excavation and repair work |

Clearly mark excavation area with cautionary sign boards (e.g. “man at work”)

| Assign CETP engineer to supervise, if carried out by contractor | marker, barriers, flags, boards |
| --- | --- |
| 2.2. | Man-holes | Gas poisoning due to presence of H2S |

Preferably, procure man-hole cleaning equipment to avoid entering of workers into man-holes at all

Check presence of gas and, if required, ventilate man hole before entering

Person entering to be secured with life line, loose end held by person outside the man hole

Person always to wear mask connected to air supply system

Lead acetate paper or H2S detection instrument

Life line and belt

Air supply system

Separate first aid kit (including Amyl Nitrite capsule) to be part of collection maintenance kit

Injuries due to falls in open and unguarded man-holes

Ensure proper cover of man-holes

| Secure open man-holes while work on-going | markers, barriers, flags |
| --- | --- |
| Suffocation die to small man-hole diameter | Proper design and installation of man-holes as per regulations (at least 60 millimeter diameter) |
|  | 2.3. | Pumps | Electrocution due to loose wires, open connections, missing and improper earthing |

Work to be carried out by qualified (licensed) contractors

| Regular checks of installations and equipment | insulation mats |
| --- | --- |
| Injuries during repair work due to improper lifting of pumps as well as due unguarded pump parts |

Check technical specifications an maintenance of lifting device

Person to keep clear of load while lifting

Guards on pump drives to be kept in place

| Sl. No | Area of operation | Anticipated risk | Recommended OSH practices | Inputs needed |
| --- | --- | --- | --- | --- |
| 3. | CETP/ETP |
|  | 3.1. | Receiving sump and screen chamber |
| Preferably, entering of workers into man-holes to be avoided at all. Installation of mechanical screens instead of manual cleaning to be considered. |
|  | Gas poisoning due to presence of H2S |

Check presence of gas and, if required, ventilate chamber before entering

Person entering to be secured with life line, loose end held by person outside the man hole

Person always to wear mask connected to air supply system

lead acetate paper or H2S detection instrument

life line and belt

air supply system

Skin diseases due to exposure of skins and body parts during cleaning/maintenance work

Use equipment such as rake and shovels

Provide and use personal protective equipment (gloves, footwear, full body apron or full body PVC suit

Wash after completion of work at screen chamber

rakes with long handles

personal protective equipment

Injuries and drowning due to falls/slips into unguarded receiving sumps/pits

Provide cover or fence type railing around and ensure these are in place all the time

| Provide rescuing equipment next to receiving area (location marked) | life buoy with life line |
| --- | --- |
| 3.2. | Equalisation tank | Injuries and drowning due to falls/slips into unguarded tanks |

Provide fence type railings and toe rails for all walk ways and platforms

Ensure these are in place all the time and not corroded

| Provide rescuing equipment on platform (location marked) | life buoy with life line |
| --- | --- |
| Injuries during repair work due to improper lifting of aerators, etc. |

Check technical specifications an maintenance of lifting device

Person to keep clear of load while lifting

Persons entering ET die fix rope/chain to be secured with life-line

safety harness and life line

personal protective equipment (helmet, gloves)

Electrocution due to loose wires, open connections, improper and missing earthing

Adequate wiring and electrical installation suitable for corrosive conditions (due to H2S).

Frequently check connections and conditions of wires and, if required, replace immediately

use starter boxes made of plastic

use fully covered earthing wires

install circuit breakers and not fuses

| Sl. No | Area of operation | Anticipated risk | Recommended OSH practices | Inputs needed |
| --- | --- | --- | --- | --- |
| 3.3. |

Chemical treatment:

(a) Flash mixer

|  | Skin burns, eye irritation due to spillage of chemicals (unhydrated lime, acidic alum solution) |
| --- | --- |

Installation of mechanical dosing system

Keep clear from chemical slurry while being added

| Worker to wear personal protective equipment such as gloves, goggles, while mixing, dosing or monitoring | personal protective equipment |
| --- | --- |
|  | (b) Clariflocculator | Injuries and drowning due to falls/slips into unguarded tanks |

Provide fence type railings and toe rails for all walk ways and platforms

Ensure these are in place all the time and not corroded

| Provide rescuing equipment on platform (location marked) | life buoy with life line |
| --- | --- |
| Injuries due to unguarded drive and gears of mechanical parts |

Provide covers for moving machine parts

| Guard approach to gears (gear box, reduction gear, prime mover) |
| --- |
|  | Electrocution due to loose wires, open connections, improper and missing earthing |

Adequate wiring and electrical installation suitable for corrosive conditions.

| Frequently check connections and conditions of wires and, if required, replace immediately |
| --- |
|  | 3.4. | Biological treatment | Injuries and drowning due to falls/slips into unguarded tanks |

Provide fence type railings (protected against corrosion) and toe rails for all walk ways and platforms

Ensure these are in place all the time and not corroded

| Provide rescuing equipment on platform (location marked) | life buoy with life line |
| --- | --- |
| Respiratory problems due to aerosols/foams |

Ensure proper submergence of aerators

Ensure proper free board in tanks

Control foam by spray water jets and anti-foaming agents

Do not assign workers showing allergic reactions to aerosols

Provide masks (suitable against organic vapours/aerosols) to workers

Affix cautionary sign “use personal protective equipment”

water jet system

personal protective equipment

Injuries due to slippery walkways caused by spillage/foam

Provide for adequate free board

Control foam by spray water jets

Frequently flush walkways

Affix cautionary sign “slippery floor”

| Sl. No | Area of operation | Anticipated risk | Recommended OSH practices | Inputs needed |
| --- | --- | --- | --- | --- |
| 3.4. | contn. | Injuries due to unguarded drive and gears of mechanical parts |

Provide covers for moving machine parts

| Guard approach to gears (gear box, reduction gear, prime mover) |
| --- |
|  | Electrocution due to loose wires, open connections, improper and missing earthing |

Adequate wiring and electrical installation suitable for corrosive conditions.

| Frequently check connections and conditions of wires and, if required, replace immediately |
| --- |
|  | 3.5. | Pipeline and pumping (valves chambers, pipes) | Injuries due to falls/slips into unguarded openings |

Provide covers on all openings or fence adequately

|  | Suffocation in valve chambers due to lack of oxygen |
| --- | --- |

Provide spindles for manually operate valve chambers

Ensure adequate size valve chambers for maintenance work

| Properly ventilate valve chamber before entering |
| --- |
|  | 3.6. | Sludge management |
| (a) Sludge thickener | Injuries and drowning due to falls/slips into unguarded tanks |

Provide fence type railings and toe rails for all walk ways and platforms

Ensure these are in place all the time and not corroded

Restrict admission to platforms

| Provide rescuing equipment on platform (location marked) | life buoy with life line |
| --- | --- |
| Injuries due to unguarded drive and gears of mechanical parts |

Provide covers for moving machine parts

| Guard approach to gears (gear box, reduction gear, prime mover) |
| --- |
|  | Electrocution due to loose wires, open connections, improper and missing earthing |

Adequate wiring and electrical installation suitable for corrosive conditions.

| Frequently check connections and conditions of wires and, if required, replace immediately |
| --- |
| (b) Mechanical dewatering equipment | Injuries due to unguarded machine parts |

Provide covers for moving machine parts

| Guard approach to gears (gear box, reduction gear, prime mover) |
| --- |
|  | Electrocution due to loose wires, open connections, improper and missing earthing |

Adequate wiring and electrical installation suitable for corrosive conditions.

| Frequently check connections and conditions of wires and, if required, replace immediately |
| --- |
|  | Hearing impairment due to noise generation | Provide hearing protection to machine operators | personal protective equipment |

| Sl. No | Area of operation | Anticipated risk | Recommended OSH practices | Inputs needed |
| --- | --- | --- | --- | --- |
| 3.6. | c) Sludge handling | Skin ailments due to chemicals present in sludge |

Consider mechanical handling as far as possible

Provide adequate protective equipment to workers

| If done by contractor, ensure workers are provided with personal protective equipment | personal protective equipment |
| --- | --- |
| 4. | Chemical management |
|  | 4.1. | Chemical storage | Respiratory diseases and skin diseases due (chemical dust) |

Arrange supply of lime powder in canvas bags

Install and maintain proper ventilation in chemical store

Provide dust mask and goggles to workers engaged in handling lime powder bags

Provide personal protective equipment to workers handling acidic alum solutions

| Affix appropriate warning sign “ use personal protective equipment” | personal protective equipment |
| --- | --- |
| 4.2. | Chemical preparation and dosing | Skin burns and irritation of eyes due to lime spillage |

If feasible, provide closed dosing system.

Provide tools for handling of chemicals

Provide personal protective equipment to workers

handling tools

personal protective equipment

Respiratory diseases and skin diseases

Install and maintain proper ventilation in chemical store

Reduce exposure time of workers in chemical dosing area

Provide personal protective equipment to workers

| Affix appropriate warning sign “use personal protective equipment” | personal protective equipment |
| --- | --- |

Injuries from falls/slips due to slippery floor conditions

Prevent leakage from dosing pumps and pillage from mixing tanks

Install drainage around mixing units

Ensure regular flushing and washing of floors

Install non-slippery and sloped flooring

| Sl. No | Area of operation | Anticipated risk | Recommended OSH practices | Inputs needed |
| --- | --- | --- | --- | --- |
| 5. | Laboratory | Skin burns/eye irritation to due to laboratory chemicals |

Always use personal protective laboratory equipment

Visibly display laboratory safety regulations and ensure proper labelling of all chemicals

Restrict admission to laboratory to authorised persons only

Provide separate training to all persons engaged in laboratory

Display boards explaining first aid and other emergency measures

Keep special emergency equipment ready (eye and skin rinsing facility)

personal protective laboratory equipment

laboratory first-aid kit

eye and skin rinsing facilities

Chemical poisoning due to accidental consumption of chemicals

Keep necessary antidotes ready in separate first aid lit

Train all laboratory staff on first aid measures

Prohibit consumption of any food and drinks in laboratory area (sign board!)

| Insist of basic hygiene of all persons engaged in laboratory work |
| --- |
|  | Respiratory problems due to inhalation of toxic fumes/gases/vapours |

Install proper fume cabinet or cup board

Provide adequate ventilation of laboratory

| Keep oxygen respirator ready | respirator |
| --- | --- |
| Risk of (chemical) fire |

Provide and maintain proper ventilation of laboratory

| Keep fire extinguisher (DCP) and sand buckets ready in and outside laboratory room | fire fighting equipment |
| --- | --- |
| 6. | Electrical supply |
|  | 6.1. | MCC room | Injuries and burns due to electrical fires and explosions |

Regularly check all electrical installations

Provide insulation mats and proper anti-static tools

Provide proper ventilation to dissipate heat from MCC room

Affix “no-smoking sign” in and outside MCC room

insulation mats

adequate tools

Electrocution

Work to be carried out only by qualified contractors and workers

Regular checks of installations and equipment

Display first aid measures

Train concerned personnel in electrical safety and emergency measures

| Keep rescue equipment and suitable fire fighting equipment readily available | electrical rescue equipment (pole with hook) |
| --- | --- |

| Sl. No | Area of operation | Anticipated risk | Recommended OSH practices | Inputs needed |
| --- | --- | --- | --- | --- |
| 6.2. | DG room | Injuries and burns due to explosion and fire |

Ensure DG alternator is covered

Train concerned personnel on electrical safety and emergency aspects including first aid

Display safety card showing name and address of nearest doctor

Ensure proper ventilation of DG room to dissipate fumes and heat

Provide well-maintained fire fighting equipment outside DG room

Install and place proper fuel storage (tank) outside DG room

| Affix “no-smoking” sign in and outside DG room | fire fighting equipment |
| --- | --- |
| 6.3. | Electrical installations | Electrocutions, burns | All installations in the CETP shall comply with IP55 standard. |
|  | 7. | Administration | Fainting due to bad air |

Provide adequate ventilation

Keep offices away from receiving sump of CETP/ETP